## Slide 1: CEE 6501 Final Project
By: Wynn Harrow

## Slide 2: Presentation outline
GitHub and Code Structure
User Input
DSM Solver Workflow
Validations
Complex Structure Study

## Slide 3: GitHub and code structure

## Slide 4: User input
x, y, z
ux, uy, uz, rx, ry, rz
Fx, Fy, Fz, Mx, My, Mz

## Slide 5: User input
ux, uy, uz, rx, ry, rz

## Slide 6: DSM Solver Workflow
Reads the .json input files
Define Global Degrees of Freedom (DOF)
Element-Level Calculations
Compute Equivalent Nodal Loads (FEFs)
Assemble Global System
Build Global Load Vector
Apply Boundary Conditions
Solve System of Equations
Compute Support Reactions
Recover Element Forces
Post-Processing & Output

## Slide 7: Validation
Example 1 Example 2

## Slide 8: Example 1
Analytical Results Computational Results

## Slide 9: Example 2
Analytical Results Computational Results
Results are close but not exact
Differences due to:
  3D model vs 2D hand calculation
  Additional DOFs
  Modeling input

## Slide 10: Complex structure study
High Line Moynihan Connector
Located in NYC (2023)
Two Sections (Steel Viaduct and Timber Bridge)
260 ft span, 20ft height, 15.5 ft width
Frame Elements for main longitudinal and transverse members
Truss Elements assigned to diagonal members
Why?
Take a bridge and apply truss and frame elements
Perform Two Case Studies
  Case 1: What are the effects during a Polar Vortex?
  Case 2: What if received a bad batch of timber

## Slide 11: Key decisions
Structural Idealization
  Modeled bridge using 3D frame + truss elements
Element Type Selection
  Allowed users more flexibility in choosing member type
Boundary Conditions
  Fixed DOFs [ux, uy, uz, rx, ry, rz] where base nodes fully restrained
Geometry Simplification
Material Assumptions
  Linear Elastic Behavior
  E, A, I assumptions
Load Case Selection

## Slide 12: Loads applied
Applied 2 kips at each node for gravity loads (pedestrians and deck weight)
Applied additional -0.5 kip/ft member gravity loads
Applied -0.15 kip/ft transverse loads (wind)
Loads were chosen as realistic approximations based on typical bridge loading, then simplified

## Slide 13: Base structure results
Largest displacement: -0.461 ft in the transverse (y) direction
Result is unexpected
Gravity load should be governing
Structure Input Possibilities
Largest Axial Load: 404 kips

## Slide 14: Case 1 results
Polar vortex dropping temperatures to -40 degrees Fahrenheit
Assuming Delta T change of 100 degrees colder
Largest displacement: -0.642 ft (very similar to base study)
Largest axial load: 654 kips (significantly higher than base study)
Key things learned:
  While being fully restrained, members will want to contract
  adding additional axial stress on the members
  Overall shape of the structure will stay relatively the same

## Slide 15: Case 2 results
Bad batch of timber / termite infestation
Modified some members to have lower stiffness
  Switched primary members to have 0.3*E
  Removed one beam on the bottom 0*E
Possible to replace without adding additional support?
Max displacement: -0.816 ft (2x more than base case)
Maximum axial force: 433 kips
Key things learned:
  Reducing stiffness increases displacement significantly
  Load redistributes to remaining members